## Slide 1
PARYAVARAN AI
AI Powered Sustainable Smart Bus Stand

## Slide 2
PARYAVARAN AI | SMART CITY INFRASTRUCTURE
The Core Problems in Public Transit
Wasted Electricity
Conventional bus stands keep lights and fans running continuously even when completely empty.
Overflowing Dustbins
Bins lack real-time sensors, leading to unhygienic conditions and delayed clearing.
Unmonitored Pollution
Air Quality Index (AQI) and heat stress levels are ignored in public waiting spots.
Passive Infrastructure
Existing bus stands lack intelligent decision-making, IoT connectivity, or data logging.

## Slide 3
PARYAVARAN AI | SMART CITY INFRASTRUCTURE
Project Key Objectives
Smart Energy Saving
Reduce power consumption using passenger-detecting IR & LDR sensors.
Environmental Health
Track Air Quality (MQ135) and temperature (DHT11) in real-time.
Automated Comfort
Activate fans and safety lighting intelligently based on live occupancy.
Data Logging & ML
Generate clean CSV datasets to train predictive Machine Learning models.

## Slide 4
PARYAVARAN AI | SMART CITY INFRASTRUCTURE
Hardware System Architecture
Microcontroller
Arduino UNO processes sensor inputs and drives relays.
Environment Sensors
DHT11 (Temp/Humidity) & MQ135 (Air Quality).
Occupancy & Range
IR Sensor (Passenger presence) & Ultrasonic HC-SR04 (Dustbin level).
Actuators & Controls
5V Relays, Cooling Fan, Safety Lights, Buzzer & Traffic Status Module.

## Slide 5
PARYAVARAN AI | SMART CITY INFRASTRUCTURE
Explainable AI (XAI) Dashboard Logic
Rule-Based Intelligence
System evaluates multi-sensor thresholds before taking action.
XAI Transparency
Dashboard explains WHY decisions were made (e.g., Fan ON because Temp > 30°C AND Passenger Present).
Confidence Score
Outputs confidence percentages for system recommendations (e.g., 92% confidence).
Operator Trust
Eliminates black-box automation by giving clear reasoning to city operators.

## Slide 6
PARYAVARAN AI | SMART CITY INFRASTRUCTURE
Ternary Environmental Logic
State +1 (Green)
Optimal Environment: Clean air, normal temp, low energy state.
State 0 (Yellow)
Moderate Caution: Raised temperature or moderate AQI warning.
State -1 (Red)
Critical Alert: High pollution detected or overflowing dustbin level.
Better Than Binary
Provides 3 intuitive status conditions instead of simple ON/OFF binary states.

## Slide 7
PARYAVARAN AI | SMART CITY INFRASTRUCTURE
Dataset Pipeline & Research Roadmap
Automated Logging
Logs sensor values, occupancy, and AI scores every 2 seconds into CSV.
Model Evaluation
Compares Decision Trees, Random Forest, XGBoost, SVM, and KNN.
Accuracy Optimization
Determines which algorithm predicts energy saving potential most accurately.
Academic Goal
Paves the way for a published research paper on AI smart infrastructure.

## Slide 8
PARYAVARAN AI | SMART CITY INFRASTRUCTURE
Expected Impact & Results
Energy Saved
~42% reduction in electricity waste recorded during testing.
Instant Response
Automated lighting and fan response within 500ms of passenger detection.
Predictive Waste Mgmt
Alerts authorities before dustbins reach 90% capacity.
Smart City Ready
Low-cost model easily scalable using ESP32 and TinyML.